## Slide 1: Module 2 Planning and deploying Microsoft Teams Android devices
<Name>
<Title>
Notes: Last reviewed – 27-APRIL-2023-MB

## Slide 2: Version history
Version | Changes | Date
2.0 | Initial release | 7th October, 2022
2.1 | Updates to licensing. Only Teams Rooms licences supported on Teams Rooms devices. | 27th April 2023
Hidden

## Slide 3: Objectives
Deploying devices throughout your organization
Selecting the right devices for your users and spaces
Understand how to create resource accounts and assign phone numbers

## Slide 4: Feature availability icons
Available
Partial
Not available
Teams phones
Teams displays
Microsoft Teams Rooms
Teams panels
Notes: When a new feature or topic is introduced, these icons will appear on the slide.
If there is a clear background, then that feature does applies to that device type
If there is a partial line, the feature is available on certain models of a device, but not others.
Example: If there is a device with a specific hardware feature such as camera.
If there is a purple background, the feature is NOT available for that device type.

## Slide 5: Deploying Microsoft Teams on Android devices

## Slide 6: Envision personal device deployment
Standardize device definitions
Desk phone or Teams display
Handset/Speakerphone
Meeting join capabilities
Options
Camera
Sidecar
Notes: Desk Phones or Teams Display? Each has different capabilities. You wouldn’t want to put a Teams Display in a common area as an example. Are you going to use handsets or speakerphones? What personas need handsets or speakerphones? Could Bluetooth paired handsets or speakerphones help here?
Meeting Join Capabilities – do they need audio/video or just audio? Do they need to join meetings and view screen sharing? Some devices don’t support all capabilities so checking this is important.
Options – do they need a camera, or sidecar? Build your personas and standardize around this.

## Slide 7: Envision Teams Rooms deployment
Standardize meeting room definitions
Size
Layout
Number of people
Desired modalities
Options
Teams panels
Teams Rooms console
Touch enabled display
Notes: For Teams Rooms – what is the size of the room? Small medium large? Based upon the size, what device would fit in and make sense?
How many people would you expect to be in the room, what’s the best layout?
Desired modalities – do you want to use audio/video? Is a laptop sharing content important? On MTRA the Touch Console is optional.
Teams Panels – do you want a device sitting outside a room to see whether the room is in a meeting or not, or ad-hoc book the room to reserve? Work in and use the room for the time it’s scheduled.
Teams Certified Devices - ensure you use certified devices for the best experience.

## Slide 8: Device selection | Phones and displays
Call center
Basic phone, large screen
Information
Worker
Teams display
Productivity phone
Executive
Teams display
Feature rich video phone
Sidecar for delegates
Shared space
Basic phone, small screen
Conference phone
Retail
Basic phone, medium screen
Notes: What phone model works best for my user? This is a common question before buying the phone. Consider the user persona and the options available.
WE have phones that have touch screens smaller than 5 inches, medium sized phones around 5” inches and Large screen phones >7 inches
If you have a call center user or a calling intensive user, a large screen phone may make sense given that they’re working that display constantly in a high call environment.
For Informational Workers, a Teams Display or a Productivity Phone would be recommended.
For some Executives, a Feature Rich Video Phone or display works really well for joining meetings on the device with video and for participating in conversations with a high-quality endpoint. Sidecars are recommended for boss/admin scenarios.
Shared spaces – a basic phone with a small screen would work great.
Retail Environment – basic phone with a medium size screen. Doesn’t need to be as big, and shouldn’t be ridiculously hard to use. Some phones do have black and white displays, so consider this also.
-----------------------------------
This is a bit of a decision tree. Given the persona, the recommended phone type is provided. Note that in many of these scenarios, headsets or speakerphones are also viable alternatives.
Small screen is less than 5 inches
Medium screen Is 5 inch + inches
Large screen Is >7 inches
Call Center – doesn’t need a top of the range device. Possibly a headset for the high use all day. A large screen is recommended given they’re working that display constantly in a high call environment.
Information Worker – Teams Display or Productivity Phone.
Executive – Teams Display. Feature Rich Video Phone for joining meetings on the device and participating in meetings with a high-quality endpoint. Sidecars used for boss/admin scenario.
Shared spaces – Basic phone with a small screen, example – common area phone. Conference phone for calling only phone scenarios such as CP960 or Poly C60.
Retail Environment – basic phone with a medium size screen. Doesn’t need to be as big, and shouldn’t be ridiculously hard to use. Some phones do have black and white displays, so consider this also.

## Slide 9: Device selection | Teams Rooms
Executive
Resource account
Executive office
Single touch-enabled display
Integrated
Shared space
Resource account
Console or remote control
Single or dual display
Integrated or modular
Teams panel
Notes: Resource accounts have an “Exchange resource” mailbox as opposed to a traditional end user mailbox.
An integrated (single unit) Teams Rooms is easy to connect and deploy for executive spaces. For Shared spaced, pick what fits best.
Teams Panels make little sense in a home office. Or even a regular office. But hey, if they are a big timer, go for it!

## Slide 10: Account types
User
Used by end users who will answer calls, be a delegate, or be in a call queue
Common area
Used for devices that are not owned by any single person, such as a phone in a kitchen or lobby
Meeting room
Used for devices that are shared among many people, such as Teams Rooms and Teams panels.
Notes: Clarify that there are three primary account types. Licenses don’t necessarily need to match the Account Types but it is highly recommended. Depending on the type of account, the User Interface on a given device can be different, adding/removing certain features or menus depending on the user.
Common Area – not owned by anyone. Typically deployed for a functional purpose.
Meeting Room – generally dedicated spaces. A device that’s used by many people to hold meetings and can be bookable. Chat about Teams Rooms Basic and Teams Rooms Pro

## Slide 11: Use distributor logistics best practices
Avoid multiple sources, centralize where possible
Ship to central location, if needed
Plan for product delays
Deployment schedules are a life saver!
Request MAC addresses if provisioning devices remotely
Notes: More good tips for standardizing.

## Slide 12: Developing a standardized deployment
Account provisioning hand-off
Create and configure accounts in advance
Use remote provisioning where possible for ease of deployment
Create and communicate standards
Step-by-step instructions
Cable dressing
Mounting locations and methods
Device setup instructions and configuration profiles
Basic troubleshooting
Operations
Microsoft Teams is great for ongoing cross-team coordination!
Have clear escalation paths during this critical time
Installation
Notes: Use Teams! Create a Teams Rooms channels for each device type and store all documentation there.
The last point is important. Who is responsible for certain parts of the implementation?
Step By Step Instructions – think for the deployment engineers/staff.
Cable Dressing – keep it clean, same as mounting locations and methods.
Make sure you have standardized documentation and that it’s referenced by support.
Have clear escalation paths. Does it go to the Identity Team, Office 365 Team? Is the helpdesk empowered to change the device?
Operations

## Slide 13: Training and enablement
User training
IT training
Awareness
Notes: User Training – produce videos, share adoption content.
IT Training - Networking will need to know about device capabilities and features. Think video, screen sharing.
Awareness – Quick Start Guides on a wall in the room. Marketing campaigns about the devices that kind of thing.

## Slide 14: Operational readiness
Device repair
Out of service
Helpdesk readiness
Notes: Ensure you’re operationally ready.
Do you have processes for device swap outs? Think logistics, on-site technicians, and service contracts with vendors.
Out of Service – how are you going to mark the room or device out of service? Cancellation of appointments, marking as OOS on room management systems, and the reverse when it’s working again!
Helpdesk Readiness – ensure your helpdesk can take tickets. Leave labels in rooms to report problems with numbers, and ensure your helpdesk have processes to route tickets accordingly.

## Slide 15: Network bandwidth planning
Determine and organize network requirements for connecting Microsoft Teams users across your organization.
Network Planner calculates your network requirements for deploying Teams and cloud voice across your organization's physical locations.
https://aka.ms/TeamsRoomsLearning
Notes: Network bandwidth Planning is extremely important. With not enough bandwidth – or a poor network in general – Teams media can be very negatively impacted.
The Teams Rooms Foundations training has a full module dedicated to just this topic – https://aka.ms/TeamsRoomsLearning
Networking impacts user perception. Ensure your network has enough bandwidth and is sized accordingly. Design for scale and your use cases. The higher quality the video, the more bandwidth that’s needed.

## Slide 16: Network connectivity testing
OneDrive, Outlook, and Teams report network metrics to the tenant
The metrics are aggregated to a geographic region, allowing administrators to see network performance
You can manually run a test at connectivity.office.com
Notes: The M365 Admin Center now helps aggregate the data of the OD/Outlook/Teams client network metrics to help admins determine where hot spots are in their network.
Read more here: Network connectivity in the Microsoft 365 Admin Center (preview) - Microsoft 365 Enterprise | Microsoft Docs
You can also manually run tests at the connectivity.office.com website.
Also – bypass proxies for Teams Media!

## Slide 17: Physical security
Security isn’t just software, it’s physical too.
Assess where you deploy your devices and understand the risks.
Deploy physical locks, disable ports, install in locked cabinets, etc.
Notes: Security isn’t just software, think physical requirements too.
Device Placement – is a device safe in an area that isn’t secured? Could a device be stolen, or used to hop to somewhere else in your network?
Hardening – block some features. Meeting Privacy – would you want a panel to say “Acquisition of Company X?” and be seen by everyone in the company walking down the hall?

## Slide 18: Shared devices resource account

## Slide 19: Resource account
This account can sign into multiple device types, such as Teams Rooms and Teams display
Must be Microsoft Teams enabled
Consider enabling for telephony, as appropriate
For Teams Rooms, this is the account that you invite to meetings
Establish a naming convention
Notes: Make sure UPN=SMTP=SIP
If all 3 don't match, the device will either fail to sign into Teams or fail to sign into Exchange.
A naming convention will help in grouping these devices in AD or Intune
Consider enabling for telephony – do all accounts need external access? Naming Convention – super important! Finding the accounts is key in your global address list. Configure a Room List in Exchange and/or Room Finder.

## Slide 20: Resource account
Teams Rooms requires its own unique account for each space
One account should be shared between all devices in a space – Teams Rooms, console, and Teams panel
It is recommended to create the account in advance of hardware installation
You can create account via:
Microsoft 365 admin center
PowerShell
Notes: Ensure you plan your resource accounts accordingly.
Create them using PowerShell or M365. Create your accounts in advance.

## Slide 21: Resource account security
Uses modern authentication
Conditional Access (CA) policies
  Recommend using different CA policies for Device accounts than other User accounts
    Location based CA policy for device accounts
    Microsoft Teams, Exchange, & SharePoint Online CA policies should match
    Do not enforce multi-factor authentication or Sign in Frequency for device accounts
    Do not enforce "Require compliant device" condition for devices with Hotdesking capability
  Do not enforce password expiry for device accounts
Sign-in token secured on device
Optional calendar processing for Teams Rooms and Panels
  Optional settings using the Set-CalendarProcessing Cmdlet
  ProcessExternalMeetingMessages, DeleteSubject, DeleteNonCalendarItems, DeleteAttachments, AddAdditionalResponse, AddOrganizerToSubject
Notes: CAP doesn’t have an Exchange mailbox, so this only applies to Teams Rooms.
We recommend using CA Policies for account security.
Location Based CA Policy – lock the account down so it can’t log in from a non trusted location.
If deploying hot desking, use Location Based CA where possible. Require Compliant Device rules don’t work well with hotdesking capabilities.

## Slide 22: Create Common Area Phone resource account
Notes: A sample Room Selection Survey is available with these presentations to share with attendees.
This type of account does not have a mailbox associated with it.

## Slide 23: Microsoft 365 admin center
Add Common Area Phone account
Navigate to Users -> Active Users
Click on Add a user
Notes: Capacity is optional, Location is optional, and honestly don’t recommend setting a Phone Number as this does *not* assign a phone number, it just adds an entry into AAD.

## Slide 24: Microsoft 365 admin center
Add Common Area Phone account
Fill in appropriate values
Do not select Require this user to change their password when they first sign in
Notes: Capacity is optional, Location is optional, and honestly don’t recommend setting a Phone Number as this does *not* assign a phone number, it just adds an entry into AAD.
Naming Conventions are important for the username, for maintenance purposes.

## Slide 25: Microsoft 365 admin center
Add Common Area Phone account
Assign Microsoft Teams Shared Devices license
Assign calling plan license
If you are using Microsoft Phone System Direct Routing or Operator Connect, you do not need to assign a Calling Plan license.
Notes: When creating the account, assign the common area phone license. You don’t have to assign a calling plan license if you don’t want to use Microsoft as your provider, you can assign a number to it from direct routing.

## Slide 26: Microsoft 365 admin center
Add Common Area Phone account
Skip Optional settings
Review settings
Click Finish adding to create account
Notes: When you’re happy, click finish adding and then create the account.

## Slide 27: Manually provisioning resource account
PowerShell can expedite resource account provisioning as well as add users in bulk.
Prerequisites
Azure Active Directory PowerShell for Graph module
Install-Module -Name AzureAD
Notes: only needed to set enable-csmeetingroom, only needed for Skype for Business Server

## Slide 28: Create account via PowerShell
C:> Connect-AzureAD
C:> $PasswordProfile = New-Object –TypeName Microsoft.Open.AzureAD.Model.PasswordProfile
C:> $PasswordProfile.Password = "HappyPwd123$$$"
C:> $UPN ='CAP-Kitchen1@contoso.com'
C:> $DisplayName ='Kitchen 1 Common Area Phone’
C:> $GivenName ='Kitchen 1’
C:> $Surname ='Common Area Phone’
C:> $Mailnickname ='CAP-Kitchen1’
C:> $UsageLocation = 'US'
C:> New-AzureADUser -DisplayName $DisplayName -Surname $Surname –PasswordProfile $PasswordProfile -UserPrincipalName $UPN -AccountEnabled $true -mailnickname $MailNickname
Notes: Connect-MsolService is used to connect to Azure AD.
If you copy/paste these commands, some will fail. For visual reasons, some options are prefixed by a non-breaking hyphen which PowerShell rejects. Run the cmdlet, see which option(s) error, then replace the (visually indistinguishable) non-breaking hyphen with a regular hyphen.
You can use this code and script the creation of accounts. Scripting makes this scalable when you’re creating thousands of accounts.

## Slide 29: Disable password expiration and assign license
C:> Connect-MsolService
C:> Set-AzureADUser -ObjectID $UPN -PasswordPolicies DisablePasswordExpiration
C:> Set-AzureADUser -ObjectID $UPN -UsageLocation $UsageLocation
Notes: Connect-MsolService is used to connect to Azure AD.
If you copy/paste these commands, some will fail. For visual reasons, some options are prefixed by a non-breaking hyphen which PowerShell rejects. Run the cmdlet, see which option(s) error, then replace the (visually indistinguishable) non-breaking hyphen with a regular hyphen.
You can use this code and script the creation of accounts. Scripting makes this scalable when you’re creating thousands of accounts.

## Slide 30: Assign license
C:> Set-AzureADUser -ObjectID $UPN -PasswordPolicies DisablePasswordExpiration
C:> Set-AzureADUser -ObjectID $UPN -UsageLocation $UsageLocation
C:> Get-AzureADSubscribedSku | Select -Property Sku*,ConsumedUnits -ExpandProperty PrepaidUnits | ?{$_.SkuPartNumber -like '*CAP*'}
SkuId : 295a8eb0-f78d-45c7-8b5b-1eed5ed02dff
SkuPartNumber : MCOCAP
ConsumedUnits : 4
Enabled : 25
#Create an object for a single license type
C:> $License = New-Object -TypeName Microsoft.Open.AzureAD.Model.AssignedLicense
C:> $License.SkuId = '295a8eb0-f78d-45c7-8b5b-1eed5ed02dff'
#Create an object for a multiple license type
C:> $Licenses = New-Object -TypeName Microsoft.Open.AzureAD.Model.AssignedLicenses
#Add the single license object to the multiple license object
C:> $Licenses.AddLicenses = $License
C:> Set-AzureADUserLicense -ObjectId $UPN -AssignedLicenses $Licenses
Notes: If you copy/paste these commands, some will fail. For visual reasons, some options are prefixed by a non-breaking hyphen which PowerShell rejects. Run the cmdlet, see which option(s) error, then replace the (visually indistinguishable) non-breaking hyphen with a regular hyphen.
You can use this code and script the creation of accounts. Scripting makes this scalable when you’re creating thousands of accounts.

## Slide 31: Create shared device resource account

## Slide 32: Resource account creation flow
Configure Calendar Auto Accept
Set password to not expire
Assign Teams License
Resource exists
Identify space
Create Exchange Resource
Configure device
Notes: Animated slide.
Identify the room that will host Teams Rooms
Does an Exchange Resource already exist? If not, create one
Configure calendar Auto Accept
Set the password to not expire
Assign a Teams license (Teams Rooms Premium! OK fine, Standard is cool too.)
Configure Device (sign in, assign a configuration profile, etc.)
Profit.

## Slide 33: Microsoft 365 admin center
Add resource account
Sign in to: https://admin.Microsoft.com
Navigate to Resources  Rooms & equipment
Notes: The easiest way to create an account is via M365 admin center.
Resources section is not shown by default. You’ll have to select “… Show all” to see it.
Resource accounts on Teams display for Hot desking

## Slide 34: Microsoft 365 admin center
Add resource account
See and edit current room inventory
Click +Add resource to create a new room

## Slide 35: Microsoft 365 admin center
Add resource account
Fill in appropriate values
Click Save
Notes: Capacity is optional but it is used for capacity notifications, Location is optional, and honestly don’t recommend setting a Phone Number as this does *not* assign a phone number, it just adds an entry into AAD.

## Slide 36: Microsoft 365 admin center
Add resource account
Acknowledgement that the room has been created
Notes: Click “booking options”….as seen on next slide….

## Slide 37: Microsoft 365 admin center
Review booking options
Available scheduling options
Notes: Note that Auto Accept Meeting Requests has been set.

## Slide 38: Microsoft 365 admin center
Set password
Navigate to Users -> Active Users
Click on key icon to set password
Notes: Now we’ve created an account, let’s set the password to something you know….

## Slide 39: Microsoft 365 admin center
Set password
Enter password
Do not tick the box to require a password change.
Notes: Let’s set the password to something we know, OK?
You cannot change/reset password via the Teams Rooms app interface, so ticking that box will prevent successful logins.

## Slide 40: Microsoft 365 admin center
Assign license
Navigate to Users -> Active Users
Click on Display name to see properties
Click on Licenses and apps
Notes: Let’s assign a license to the account.

## Slide 41: Microsoft 365 admin center
Assign license
Select license
Click Save changes
Notes: Teams Rooms Standard license recommended: Teams Rooms Premium license strongly recommended if you’re wanting the full managed service.

## Slide 42: Manually provisioning resource account
PowerShell can expedite resource account provisioning as well as add users in bulk.
Prerequisites
Azure Active Directory PowerShell for Graph module
Install-Module -Name AzureAD
Exchange Online PowerShell Module
Install-Module -Name ExchangeOnlineManagement
(Optional) Microsoft Teams PowerShell Module
Import-Module –Name MicrosoftTeams
Notes: Skype Online only needed to set enable-csmeetingroom, only needed for Skype on-prem or online (or if you want to join meetings via URI, e.g. blah@bluejeans.com)

## Slide 43: Manually provisioning resource account
Account name
$acctUpn='mtr-focusroom1@contoso.com'
The unique name of the mailbox
$MailBoxName='focusroom'
Specify the Exchange alias (also known as the mail nickname) for the recipient
$MailBoxAlias='focusroom'
Password for the account
$Password='ThisIs1ReallyLongPassword!'
License to assign
$ADLicense='03070f91-cc77-4c2e-b269-4a214b3698ab'
Two letter ISO code for the country where the tenant is registered
$UsageLocation='US'
Friendly name for the room
$DisplayName='Focus Room 1'
Notes: Skype Online only needed to set enable-csmeetingroom, only needed for Skype on-prem or online (or if you want to join meetings via URI, e.g. blah@bluejeans.com)
ADLicense SkuID obtained via:
Get-AzureADSubscribedSku | Select -Property Sku*,ConsumedUnits -ExpandProperty PrepaidUnits | ?{($_.SkuPartNumber -like '*Room*') -Or ($_.SkuPartNumber -Like '*MTR*')}

## Slide 44: Manually provisioning resource account
C:\> New-Mailbox -Name $acctUpn -Alias $MailBoxAlias -Room –DisplayName $DisplayName -EnableRoomMailboxAccount $true -RoomMailboxPassword (ConvertTo-SecureString -String $Password -AsPlainText -Force)
Notes: Note: Creating a mailbox of type Room. Unlike common area phone, we don’t use Azure AD to create this account. The User account is automatically created int eh background.

## Slide 45: Manually provisioning resource account
C:\> Set-CalendarProcessing -Identity $MailBoxAlias -AutomateProcessing AutoAccept ‐AddOrganizerToSubject $false -DeleteComments $false -DeleteSubject $false ‐RemovePrivateProperty $false –ProcessExternalMeetingMessages $true -AdditionalResponse 'This is a Microsoft Teams Meeting room!'
Notes: Note: Creating a mailbox of type Room. Unlike common area phone, we don’t use Azure AD to create this account. The User account is automatically created int eh background.

## Slide 46: Manually provisioning resource account
  C:\> Set-AzureADUser -ObjectID $acctUpn -PasswordPolicies DisablePasswordExpiration
  C:\> Set-AzureADUser -ObjectID ConferenceRoom01@contoso.com -UsageLocation 'US'
  #Create an object for a single license type
  C:\> $License = New-Object -TypeName Microsoft.Open.AzureAD.Model.AssignedLicense
  C:\> $License.SkuId = '6070a4c8-34c6-4937-8dfb-39bbc6397a60'
  #Create an object for a multiple license type
  C:\> $Licenses = New-Object -TypeName Microsoft.Open.AzureAD.Model.AssignedLicenses
  #Add the single license object to the multiple license object
  C:\> $Licenses.AddLicenses = $License
  #Assign the license to the resource account
  C:\> Set-AzureADUserLicense -ObjectId $UPN -AssignedLicenses $Licenses
Notes: Note: Creating a mailbox of type Room. Unlike common area phone, we don’t use Azure AD to create this account. The User account is automatically created in the background.
Get-AzureADSubscribedSku | Select -Property Sku*,ConsumedUnits -ExpandProperty PrepaidUnits | ?{($_.SkuPartNumber -like '*Room*') -Or ($_.SkuPartNumber -Like '*MTR*')}

## Slide 47: Create account via PowerShell
Connect-MsolService
Connect-ExchangeOnline
$UPN='MTR-STP-FocusRoom3@contoso.com'
$DisplayName='St. Petersburg Focus Room 3'
$MailBoxName='MTR-STP-FocusRoom3'
$MailBoxAlias='MTR-STP-FocusRoom3'
$Password=ConvertTo-SecureString 'HappyPwd!!!' -asplaintext -force
$AdditionalResponse='St. Petersburg Focus Room 3'
$UsageLocation='US'
$License='contoso:Microsoft_Teams_Rooms_Pro'
New-Mailbox -MicrosoftOnlineServicesID $UPN -Name $DisplayName -Alias $MailBoxAlias -Room ‐EnableRoomMailboxAccount $true -RoomMailboxPassword $Password
Set-CalendarProcessing -Identity $MailBoxAlias -AutomateProcessing AutoAccept -AddOrganizerToSubject $false ‐DeleteComments $false -DeleteSubject $false -RemovePrivateProperty $false -AddAdditionalResponse $true ‐AdditionalResponse $AdditionalResponse -ProcessExternalMeetingMessages $true
Set-MsolUser -UserPrincipalName $UPN -PasswordNeverExpires $true -UsageLocation $UsageLocation
Set-MsolUserLicense -UserPrincipalName $UPN -AddLicenses $License
Notes: Azure AD v1 example. So much simpler applying the license…..

## Slide 48: Sign-in

## Slide 49: Sign-in modes
Personal devices
Signs in with E3/E5 license
Registers with Intune
Provides full feature set
Hotdesking supported
Common area phone
Phones in common areas which do not require user login
Registers with Intune
No calendar support
Hotdesking supported
Meeting room
Devices in meeting rooms which do not require end user login
Registers with Intune
Optimized calendar UI
No hotdesking
Notes: There are three sign-in modes.
By default, the license assigned to a user determines which features are available.
For example:
A user with an E3 license will have whiteboard and meeting recording
A user with a Teams Rooms Standard license will not show a hotdesking option.
Using a CAP license with Teams Rooms is unsupported.
Teams Panel – you can sign in with what you want, but the UI doesn’t change.

## Slide 50: Sign-in modes
Phone UI Comparison
Personal devices
Signs in with E3/E5 license
Common area phone
Phones in common areas which do not require user login
Notes: This shows the various changes to the UI based on the license assigned to the user signing in.

## Slide 51: Sign-in modes
You can override license auto-detection.
Create and assign new policies using:
New-CsTeamsIPPhonePolicy and
Grant-CsTeamsIPPhonePolicy
C:\> New-CsTeamsIPPhonePolicy –Identity 'Meeting Sign in' –Description 'Meeting Sign In Phone Policy' -SignInMode MeetingSignIn
C:\> Grant-CsTeamsIPPhonePolicy –Identity adelev@contoso.com –PolicyName 'Meeting Sign In'
Notes: Full PowerShell to “convert” an E5 license to emulate a Meeting Room Standard license.
Import-Module MicrosoftTeams
$sfbSession = New-CsOnlineSession
Import-PSSession $sfbSession
New-CsTeamsIPPhonePolicy -Identity "Meeting Room Sign In" -Description "Meeting Room Sign In Phone Policy" -SignInMode MeetingSignIn
Grant-CsTeamsIPPhonePolicy -Identity mtr-stp-townview-1@contoso.com -PolicyName "Meeting Room Sign In"

## Slide 52: Web sign-in
Notes: When you boot the phone, you are brought to this screen which generates a code.. Open web browser to microsoft.com/devicelogin

## Slide 53: Web sign-in
ERNRZR72J
adelev@contoso.com
Notes: Open web browser to microsoft.com/devicelogin and enter the code.
It then asks us for a username and password, and then sign in.

## Slide 54: Web sign-in
Notes: Phone showing sign in is working.

## Slide 55: Remote provisioning

## Slide 56: Remote provisioning
Remotely provision and sign into a Teams device using Teams admin center
Add an individual device via MAC address or upload a csv file to add devices in bulk
Notes: One of the most popular asks in terms of features for phone deployment is the ability to remotely provision and sign into teams devuces from the admin center. recently we published a feature that allowed tenant admins to do just that. IT admins can now remotely provision & sign into a teams Android device from the teams admin center. Let's walk through the experience to do it. before starting the provisioning be aware that this feature requires a baseline minimum firmware on the device. Work with your OEM vendors to get devices with the baseline firmware.
To do this the admin has to upload a set of device Mac addresses that are going to be deployed in their tenant to the admin center along with the location where they want to deploy the device. This can be entered one by one or can be uploaded in bulk using a CSV file.
-------------------------
A device could have 2 MAC addresses – Ethernet and WiFi. Be sure to add the correct one. Or both, then go back and remove the one that wasn’t used.

## Slide 57: Remote provisioning
Select devices to provision and click Generate verification code
Notes: Once devices added, click Generate verification code. You will read this code to the on-site technician.

## Slide 58: Remote provisioning
Notes: On site technician powers on device, hits settings cog, and select Provision phone.

## Slide 59: Remote provisioning
913997
Notes: A device could have 2 MAC addresses – Ethernet and WiFi. Be sure to add the correct one. Or both, then go back and remove the one that wasn’t used.

## Slide 60: Remote provisioning
Teams admin center
Notes: Once the MAC ID is uploaded to the admin center a technician typically sets up the device in the assigned location. After the technician completes OOBE, as a one time security feature, the technician has to enter a verification code on the device after it is connected to the network. The verification code is generated on the teams admin center by the tenant admin. As soon as verification is complete the device is available for remote sign in on the admin center as you can see here on the left pin. Once you click on sign in the instructions to remotely sign into the device are provided as shown in the right pane the tenant admin goes to microsoft.com/devicelogin and enters the code that is available on the admin center once this is validated the tenant admin science into the shared space device with the credentials that is reserved for this device.
----------------------
Phone now shows a message stating that the admin is signing in.
In Teams admin center, copy the code and get ready to paste it in to microsoft.com/devicelogin

## Slide 61: Remote provisioning
FPLGJZYH
CAP-Lobby1@contoso.com
Notes: Open web browser to microsoft.com/devicelogin

## Slide 62: Remote provisioning
Notes: The website shows you logged in successfully
The phone is now signed in.
LP in the upper right are the initials of the CAP account as entered when creating the CAP account. In this case, LP = “Lobby Phone”

## Slide 63: Remote sign out
You can remotely sign out any device
From Teams admin center, navigate to the device’s properties and select Actions and then Sign out

## Slide 64: Remote sign in
You can remotely sign in any device that has already been registered to Teams admin center
From Teams admin center, navigate to the device’s properties and select Sign in
Follow the steps to complete the remote sign in (like device provisioning)

## Slide 65: Multi-cloud sign-in support
Devices now support specialized clouds.
Users can click the gear and switch to the option applicable to their tenant.
Accessed from the in settings.
Notes: If you need to sign into specialized clouds, you can now do this from the device.

## Slide 66: Assigning phone numbers

## Slide 67: Assigning phone number – calling plans
Configurable using Teams admin center
For USA and Canada, you must create an emergency location first
Notes: Calling Plans = Microsoft as your phone number provider.

## Slide 68: Assigning Calling Plan phone number - PowerShell
C:\> $UPN='MTR-SEA-FocusRoom1@contoso.com'
C:\> $PhoneNumber='+14255553223'
#Get Location ID via Get-CsOnlineLisLocation
C:\> $LocationID='c04255ef-0aac-4cc8-b5fe-510c4578f792'
C:\> Set-CsOnlineVoiceUser -Identity $UPN -TelephoneNumber $PhoneNumber -LocationID $LocationID
Notes: Note: Creating a mailbox of type Room. Unlike common area phone, we don’t use Azure AD to create this account. The User account is automatically created int eh background.

## Slide 69: Assigning phone number - PowerShell
C:\> $acctUpn='MTR-SEA-FocusRoom1@teamsroomslab.com'
C:\> $PhoneNumber='+14255553223'
#Get Location ID via Get-CsOnlineLisLocation
C:\> $LocationID='c04255ef-0aac-4cc8-b5fe-510c4578f792'
C:\> Set-CsPhoneNumberAssignment -Identity $AcctUPN -PhoneNumber $PhoneNumber -LocationID $LocationID -PhoneNumberType CallingPlan
Notes: Note: Creating a mailbox of type Room. Unlike common area phone, we don’t use Azure AD to create this account. The User account is automatically created int eh background.

## Slide 70: Assigning phone number – PowerShell
C:\> New-CsTeamsCallingPolicy -Identity NoVoiceMail -Description "Do not permit user to have voice mail" -AllowVoicemail AlwaysDisabled
C:\> Grant-CsTeamsCallingPolicy -Identity MTR-TVW-Conference1 -PolicyName NoVoiceMail
Voice mail on shared accounts is rarely monitored
Helps prevent filling up mailbox with unnecessary voice mail
Notes: Note: Creating a mailbox of type Room. Unlike common area phone, we don’t use Azure AD to create this account. The User account is automatically created int eh background.

## Slide 71: Summary

## Slide 72: Summary
Have a plan for deploying devices
Standardize on devices
Create any required accounts
Assign phone numbers as necessary
Notes: Read summary of what they learned.

## Slide 73: Questions?

## Slide 74: Thank you.